## Slide 1: Broader Impact and Requirements of Power Plants
John C. Bean
Outline
(Revised September 2024)
Some of which are cited in social media (and even respected newsfeeds)
as reasons to abandon certain established or emerging energy technologies
But those criticisms may or may not be supported by actual data and facts
And I've found more damning ones that are overlooked - Calling for a closer examination of:
Raw Materials required by Power Plants
Their natural abundance, where the are found, how they are extracted
Necessary refining of those Materials
Transportation of those Materials
From Mines & Wells to Refineries, to Power Plants
The Energy they Produce vs. Energy Invested in their Extraction, Refining and Transportation Sometimes misleadingly quantified in "Energy Payback Time" (EPBT)
But more appropriately described by "Energy Return on Invested Energy" (EROI)
Which ranges over more than a factor of ten for today's energy technologies
Unintended Consequences of some of the above, including (possibly):
Leaks, fires, ground water & aquifer contamination, desecrated landscapes . . . earthquakes

## Slide 2: Broader Impact and Requirements of Power Plants
I've compared power plant land & water requirements
And later I'll compare power plant atmospheric / global warming impacts
But other impacts & requirements are difficult to compare. A prime example:
The impact of raw material mining, refining and transportation
Why? Because different power technologies depend on very different materials
The impact of each must be separately studied
Often resulting in apple to orange to pear comparisons
This can produce a large gray information void
Filled by lavishly funded marketing campaigns for entrenched energy technologies
Or (sadly) by scientists denigrating one technology to promote their own

## Slide 3: This note set will venture into this "gray information void"
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
In a few cases, I've actually found data that support or refute a specific claim
But for the much larger number of ambiguous cases,
I can at least dig deeper into the issues and facts,
getting well beyond blogger and advertising hype
With luck, this may transform scattered orange vs. apple vs. pear claims
Into more meaningful orange to lemon to lime to grapefruit comparisons

## Slide 4: To begin: Energy production nearly always involves
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Raw materials to build power plants and/or fuel those power plants:
What are their natural abundances?
Where, and in what form, do they naturally occur?
How are they extracted from these locations?
Refining to convert these raw materials into useful forms
Transportation from mines/wells to refineries, and then to the power plant itself
Energy investment to accomplish all of the above
Unintended consequences / side-effects
Upon aquifers, rivers, the air we breathe . . .

## Slide 5: Starting with issues relating to raw material sources:
Source: http://www.webelements.com/
Which atomic elements will we need for energy production?
Probably these (that is, almost all of them):
Where must they be found? In the accessible top 1-2 miles of the earth's crust
OK, then what's in the crust, particularly the near-surface crust?

## Slide 6: The earth started out as, and pretty much still is, a molten ball
Gravity drives denser things to the center
With progressively less dense things forming shells around the denser things
Which would leave the least dense things at the surface
Where they, alone, can radiate heat into space, causing them to cool
Forming a thin solid surface scum that we call the earth's crust
Now, add in the fact that the earth is 4.5 billion years old
Giving all of those liquids a lot of time to cool and sort themselves out
From which you'd then expect the earth to be layered like an onion:
With spherical shells of pretty uniform material
Layered on top of other shells of denser material

## Slide 7: We thus expect the outermost crust layer to be rich in light elements
Source: http://www.webelements.com/
=> This wonderfully reworked version of the Periodic Table
With cell size proportional to element's crustal abundance:

## Slide 8: IN FACT: Si, O, Al, Fe, Ti, Ca, Mg, Na and K are so common
http://en.wikipedia.org/wiki/Abundance_of_elements_in_Earth%27s_crust
That we need a 12 decade semilog plot (!) to even list other crustal elements:

## Slide 9: But my Onion Earth Model omits something very important:
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Convection
Exposed outer layers of lighter materials are cooling, and thus becoming denser
Trapped inner core layers cannot radiate, and thus cannot similarly cool
In fact, the core may not cool at all because it has sucked in heavy atoms
Which include a higher proportion radioactive atoms (which tend to be heavy)
These eventually undergo "radioactive decay," meaning that they fall apart
1) Creating lighter atomic elements AND
2) Liberating massive amounts of heat
Which causes materials around them to expand
Both => Formation of less dense material in the earth's core
Gravity then drives that less dense material upward:

## Slide 10: Setting up mega convection currents:
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
These mega convection currents drag along some of the heavy elements
Disrupting the otherwise uniform layering of my Onion Earth Model
Surface flows then push chunks of crust to their sides => Plate Tectonics

## Slide 11: Plate tectonics drives subduction:
Attributed by Google Images to www.geodesy.cwu.edu – but no longer found at that URL
If convective upwelling is pushing plates apart somewhere
It must be driving them together elsewhere (e.g. where convective flows dive)
Where plates are driven together, there are only two possibilities:
1) Plate edges crumple => Mountain formation ("upthrust")
2) One plate edge burrows under the edge of the other ("subduction")
Lighter material is thus driven below heavier material

## Slide 12: As subducting lighter material heats up and melts:
Fig. 1: Triggers for the Formation of Porphyry Ore Deposits in Magmatic Arcs, J.J. Wilkinsen, Nature Geosciense 6, pp. 917-25 (2013)
http://www.nature.com/ngeo/journal/v6/n11/full/ngeo1940.html
Figs. 2 & 3: Continental-root Control on the Genesis of Magmatic Ore Deposits, W.L. Griffin et al., Nature Geoscience 6, pp. 905-10 (2013)
http://www.nature.com/ngeo/journal/v6/n11/fig_tab/ngeo1954_F4.html
Its now liquid lighter components can bubble upwards => Volcanoes
As water (w/ minerals) can percolate up through cracks => Hot springs & Geysers
Both of which can create localized surface / near-surface ORE DEPOSITS

## Slide 13: ADD TO THIS: Thin sedimentary layers produced by water & plants
http://www.thunderboltkids.co.za/Grade5/04-earth-and-beyond/chapter3.html
Water erodes away high points, washing materials into a sea or lake
Material then settles out into thin layers at their bottom
OR: Shallow sea/lake itself dissolves specific materials from the surrounding crust
Sea/lake dries out, dissolved materials => New thin layers (e.g. salt flats)
OR: The above sedimentation process buries layers of plants previously on surface

## Slide 14: Ultimately leading to crustal raw material maps such as these:
Fig. 1-23 in:
Critical Analysis of World Uranium Sources – USGS (2012)
http://pubs.usgs.gov/sir/2012/5239/
Uranium:
Overall U.S. abundance: U.S. mining regions:
http://energy.usgs.gov/portals/0/Rooms/uranium/images/uranium_concentrations.gif

## Slide 15: Oil and Natural Gases:
http://certmapper.cr.usgs.gov/data/website2011_iframes/statusmapdnn.html?state=
From a United States Geological Survey (USGS) interactive map:

## Slide 16: Coal:
http://www.earthlyissues.com/coal.htm

## Slide 17: Copper:
https://en.wikipedia.org/wiki/Copper_mining_in_the_United_States
Location of major U.S. copper mines:

## Slide 18: Aluminum:
Quotation and figure from: https://en.wikipedia.org/wiki/Bauxite
As embedded in bauxite ore, which consists of:
  "the minerals gibbsite Al(OH)3, boehmite y-AlO(OH) and diaspore a-AlO(OH), mixed with two iron oxides goethite and haematite, the clay kaolinite and small amounts of anatase TiO2"

## Slide 19: Power plants use many other materials
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
For instance, they certainly use a lot of iron
And plants like hydro & nuclear use a lot of concrete
But they account for only a small part of our TOTAL iron & concrete consumption
Even if we converted to 100% hydroelectric (as I'll prove in a later lecture)!
So while energy contributes to iron, concrete, and other raw materials use
Energy choices will not strongly affect their overall consumption
And because my goal here is to assess the impact of energy choices
I believe it's fair to limit ourselves to the raw materials listed earlier
Thus having addressed: Natural abundance? & Location?
Let's move on to: How are they extracted from these locations?

## Slide 20: If we want to minimize extraction cost AND environmental upheaval:
Left: http://auslaogroup.com/biomass/auslao-biomass/
Center: http://en.wikipedia.org/wiki/Salar_de_Atacama
Right: http://boraboraphotos.com/beautiful-white-sand-beach-in-bora-bora/
Our first choice would be for raw materials to occur right on the earth's surface!
Where we could just cut them down or scoop them up
Disturbing nothing else / Liberating nothing else
Do some of our energy raw materials occur right on the earth's surface, Yes:
Biofuels and Biomass: Lithium: Silicon:
Farms and forests Altacama Chile salt flats White sand (= quartz = SiO2)

## Slide 21: Second choice for raw material location (and form)?
Left: https://www.hcn.org/blogs/goat/los-angeles-city-council-votes-for-a-fracking-moratorium-and-hopes-california-follows-suit
Right: http://www.annarbor.com/news/saline/crude-oil-drilling-in-saline-township-paxton-resources/
Highly concentrated liquid or gas pockets
Minimizing both extraction cost and environmental disruption because:
Extraction requires only a limited number of small-footprint wells
With which we, and nature, can co-exist pretty well
At least in the short term . . . At least if no one screws up

## Slide 22: That is the classic oil / petroleum scenario
http://archive.fortune.com/galleries/2007/fortune/0704/gallery.f500_photos.fortune/4.html
But these fossil fuels start as thin layers of surface organic material
Which are buried by sediments
Which produces elevated pressure + heat => transformation
Sometimes (but not always) producing liquids and gases
If they REMAIN in thin layers, there's very little of them per land-area
And we'd need a huge number of wells to gather significant quantities

## Slide 23: So we want liquid/gas pockets, requiring two more things:
http://geology.com/stories/13/salt-domes/
1) Porous layers in the crust through which liquids and gases can move
2) Geological transformation of these originally flat layers into bulges
=> Lower density hydrocarbons then accumulate near tops of bulges
Classic location/mechanism = Salt Domes associated with oil reservoirs:
Salt & Oil start as thin flat sedimentary layers
Sediments above try to compact both
But crystal structure of salt resists compaction
Leaving it less dense than surroundings
Causing it to eventually float/bulge upward
With less dense oil also "floating along"

## Slide 24: Third choice: Big, rich, concentrated, solid pockets
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Which could then be dug out creating only a few really big holes
Which, individually, are not very nice
But we need only a small number of them
(Sometimes: One or less per nation)
And while their local environmental disruption can be massive
It is localized, and thus easier to mitigate
(at least in principle . . . if governments require it)
Driven by radioactivity, convective plumes, and plate tectonics,
Nature does provide us with variation in crustal minerals
And, every once in awhile, produces the desired concentrated local solid pockets
Which we seek out, and then dig out, in Quarries & Open Pit Mines

## Slide 25: From a listing of the worlds biggest open pit mines: 1
Bingham Canyon, Utah (Copper Ore)
Chuquicamata, Chile (Copper Ore)
Escondida, Chile (Copper Ore)
Udachny, Russia (Diamonds)
Grasburg, Indonesia (Copper & Silver Ore)
1) www.mining-technology.com/features/feature-top-ten-deepest-open-pit-mines-world/
These (NOT Egyptian Pyramids!) are biggest man-made structures seen from space
Size of those dump trucks:

## Slide 26: Shocked? Think we need to revert to pre 20/21st century technology?
John C. Bean vacation photographs
Think again: Huge quarries are not just 20/21st century technology
On a warm June day I saw what appeared to be strangely snow-covered mountains:
They were actually the Carrera marble quarries started by the Romans
And what about Rome's civilization-supporting roads and aqueducts?
Where do you think they got all of that stone?

## Slide 27: Civilizations, ancient and modern, depend upon quarries
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Even if we may not always be aware of them
For instance, see this Apple Maps satellite picture of my town of Charlottesville:
University
NEAREST QUARRY
(tree-hating housing development)

## Slide 28: Fourth & worst choice: Widely dispersed raw materials
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Likely from mostly undisturbed and un-redistributed sedimentary layers (left)
Extending for 1000's of square miles, as in U.S. coal deposits (right)
But with layers only a few meters thick (and often 100's of meters down)
So to get enough, we must (hugely) disturb 1000's of square miles!

## Slide 29: The best alternatives (for this worst alternative)?
http://www.coalcampusa.com/sowv/logan/stirrat/stirrat.htm
Environmental damage is lessened if layers are deeper and must be mined
Because, assuming mines (and mine tailings) are not too extensive,
Ecosystem (largely at surface) will be less affected
But based on economics alone, you'd probably want layers near the surface
Making them accessible via strip-mining or mountaintop-removal
Contemporary West Virginia examples of coal removal via:
Classic Mining Strip-Mining Mountaintop-Removal
http://vault.sierraclub.org/sierra/201209/mountaintop-removal-coal-mining-west-virginia-251.aspx
http://www.sourcewatch.org/index.php/Mountaintop_removal

## Slide 30: Exact differences between these three alternatives?
https://confluence.furman.edu:8443/display/GGY230F10/Surface+Mining2
Raw material (in this case coal) is all in one, or a few, thin layers
Covered by 10's or 100's of meters of other layers = "overburden"
Classic mining: Overburden is left in place (as mines burrow beneath it)
Strip-mining: Thinner overburden is instead pushed aside – into piles
Mountaintop-removal: Overburden covering whole mountain tops
is pushed aside to fill adjacent valleys

## Slide 31: Mountaintop removal can devastate entire landscapes because:
1) https://en.wikipedia.org/wiki/Mountaintop_removal_mining
and references therein cited
1) Final, full reclamation step may never occur
Due to bankruptcies AND long history of federally granted "variances" 1
2) If reclamation does occur, use of artificial organic-poor soil is allowed
=> Diminished fertility => Diminished plant and animal diversity
Persisting on the time scale of centuries 1
3) Rain flows into now crumbled valley-filling overburden
Leaching out (previously sealed in) heavy metals
Which can then massively pollute out-flowing streams 1
4) Scale and extent of mountaintop removal is huge:
"MTR will mine over 1.4 million acres (5700 square kilometers) by 2010,
an amount of land area that exceeds that of the state of Delaware." 1

## Slide 32: Satellite views of West Virginia:
1) http://gulahiyi.blogspot.com/2008_12_01_archive.html
2) http://appvoices.org/2014/08/15/its-still-happening/
"Five hundred mountains and counting . . . " 2
3) http://wvhighlands.org/wv_voice/?category_name=mining-matters&paged=31
4) http://designandviolence.moma.org/mountaintop-removal-various-designers/

## Slide 33: Similar: Tar sands (a.k.a. oil sands)
1) http://ostseis.anl.gov/guide/tarsands/ 2) https://en.wikipedia.org/wiki/Oil_sands
3) The Opposite of Mining – Tar Sand Steam Extraction, Scientific American, January 2013
4) The True Cost of Fossil Fuels, Scientific American, April 2013
"A combination of clay, sand, water, and bitumen, a heavy black viscous oil" 1
They are so viscous that they do not flow well enough to be sucked up by wells
So they've been strip mined. And once on the surface, super-heated:
By steam, from water (via burning of other oil & gas)
Until viscosity decreases to point that oil and sand can be separated 2
But more recently: Steam + solvents have just been injected into the ground 3
And hot, lower viscosity, oil/tar pumped out =>
Less land disruption / But more energy expended (plus, fate of solvents?)
Steam injection has ALSO long been used for overly viscous classic oil deposits
As for "Heavy California Oil" 4 (which shows up later in this note set)

## Slide 34: And this brings us naturally to hydraulic fracturing
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm
Known unpopularly as FRACKING
Natural gas is also produced by fossilization of organic sediments
Meaning that it is also formed in broad but thin (and thus dilute) layers
If adjacent rock layers are porous and/or fractured
Gas can migrate and accumulate => Extraction via wells (see above)
But if surrounding layers are solid, gas remains in myriad tiny separated pockets
But we can fracture that solid surrounding solid material
By pumping in fluids at extremely high pressure
Which shatters those surrounding rock layers
Complete process:

## Slide 35
https://socinnovation.wordpress.com/2014/07/05/sia-fracking/
WATER is injected at extremely high pressure to crack surrounding stone
Sand / grit is added to hold cracks open after water pressure is released
Plus other additives, including possibly:
Acids to etch and roughen crack surfaces => Preventing their tight re-closure
Solvents / detergents to dissolve oilier materials

## Slide 36: Objections to fracking?
1) Water: Previous figure claims 70-140 billions of gallons per year for the U.S.
But water is still abundant in some places
And it need not be pure: Even brackish (mildly salty) water would suffice
2) Earthquakes: Fractured rock layers can shift more easily
Triggering release of tectonic stresses (which are the real cause)
3) Cracks: Which allow not only gas to move, but anything else down there
Including, possibly, toxic heavy metals dissolving in water
4) Chemical Additives: Which can include a witch's brew of possibilities
Now chosen SECRETLY in petroleum company back rooms
Even on U.S. lands, government is only beginning to require disclosure
And is still giving companies a free hand on what they decide to add!

## Slide 37: And now we bring in aquifers:
http://modernsurvivalblog.com/retreat-living/united-states-aquifer-locations/
Which are huge broad swaths of buried, naturally fractured or porous rock layers
Into which, over many thousands of years, water has percolated
= Vast "underground lakes" supplying our drinking & farm water wells
If fracked region connects, its chemicals could be dispersed into aquifer

## Slide 38: The potential for large-scale groundwater pollution?
https://fracfocus.org/hydraulic-fracturing-how-it-works/hydraulic-fracturing-process
Current U.S. fracking sites:
With groundwater pollution already identified in Montana and Pennsylvania
(and strongly suspected elsewhere)

## Slide 39: Would-be fracking sites:
http://www.eia.gov/analysis/studies/usshalegas/
EIA map of shale gas occurrence:

## Slide 40: Things that strike me about the fracking controversy:
We (the U.S. public) are at least a bit complicit:
Torrent of fracked natural gas is what has driven down our energy prices
And has given us our much beloved sub $3 per gallon gasoline
To get this we effectively "sold our souls" by allowing:
The petroleum industry, with their long record of environmental pollution,
To secretly choose which chemicals are injected into our ground
And it's now "progress" if they just tell us what they're injecting?
And the full witch's brew of chemicals may not even be necessary:
I've read interviews with reputable energy industry sources
Who say that with water + sand/grit alone, fracking would still work
Not quite as well, not extracting quite as much gas
But still hugely productive and economically viable

## Slide 41: On to raw material transportation
p. 36:
Freight Facts and Figures 2013, Federal Highway Administration, US Department of Transportation
http://ops.fhwa.dot.gov/Freight/freight_analysis/nat_freight_stats/docs/13factsfigures/pdfs/fff2013.pdf
Where one thinks of:
Our highways And our freight railways
But highways are increasingly congested (as indicated by thickened lines at left)
Besides, who wants to drive next to a fully-loaded gasoline tanker?
However, lately, our freight railways have gone seriously off track:
http://archive.freightrailworks.org/network/class-i/

## Slide 42: Lac-Megantic Canada (near the Maine border), 6 July 2013:
http://globalnews.ca/news/2094045/two-years-later-rebuilding-after-the-lac-megantic-train-derailment/
http://www.theglobeandmail.com/news/national/lac-megantic-derailment-anatomy-of-a-disaster/article20129764/
Crude oil tank cars derailed in the town center => 1 km diameter fireball
47 people burned to death
30 buildings destroyed

## Slide 43: Railways argue that solution is just newer tougher tank cars:
1) https://en.wikipedia.org/wiki/DOT-111_tank_car
The tank cars involved were U.S. DOT-111 / Canadian CTC-111A
Which is the older, unpressurized, unreinforced "classic" tank car
Accounting for 80% of Canadian cars / 69% of U.S. cars 1
Effective 1 October 2011, U.S. DOT had revised design standards
Requiring thicker steel as well as increased shielding for filling valve head
But new standard applied only to newly constructed cars
And there was no requirement to retrofit existing cars
And no mandatory schedule for retiring older cars

## Slide 44: And rather than decreasing, derailment fires have become epidemic
1) http://www.propublica.org/article/govt-data-sharpens-focus-on-crude-oil-train-routes
Interactive map on recent railway accidents (along with enlarged keys to map): 1

## Slide 45: I caught a data-laden June 2015 CBS News story about this trend Hoping for a neutral source, I Googled "CBS News tank car derailment and fire"
1) http://daily.sightline.org/2014/05/01/new-safer-tank-cars-were-involved-in-the-lynchburg-oil-train-fire/
2) http://www.lohud.com/story/news/transit/2015/02/17/oil-train-accident/23561871/
3) http://www.chicagotribune.com/news/local/breaking/chi-galena-train-derailment-20150305-story.html
4) http://www.startribune.com/jan-8-oil-train-accidents-prompt-review-of-tank-car-safety/239194271/
5) http://www.ntsb.gov/news/press-releases/Pages/pr20150406b.aspx
March 6, 2015 - Bellevue IA
May 6, 2015 - Heimdal ND
Dec 30, 2013 - Casseldon ND
April 30, 2014 – Lynchburg VA
March 6, 2015 – Galena ILL
Feb 16, 2015 - Charleston WV
After further narrowing my search, I found:
"Newer 'safer' tank cars were involved in Lynchburg VA oil train fire" 1
"Safer tank cars on CSX train didn't prevent blast" 2
"BNSF: Oil train derailment near Galena involved safer tank cars" 3
"Oil train accidents prompt review of tank car safety" 4
Culminating with this April 6, 2015 announcement:
"NTSB Issues Urgent Recommendations Calling for Improved Rail Cars to Carry Flammable Liquids" 5
Giving me accident overload:

## Slide 46: But economics (and possibly safety) long ago stimulated an alternative
http://www.api.org/oil-and-natural-gas-overview/transporting-oil-and-natural-gas/pipeline/where-are-the-oil-pipelines
Of which you are probably not fully aware
Continent-spanning oil pipelines

## Slide 47: And gasoline pipelines:
https://www.azag.gov/consumer/gasoline

## Slide 48: And natural gas Pipelines:
http://www.eia.gov/pub/oil_gas/natural_gas/analysis_publications/ngpipeline/images/compressorMap.gif

## Slide 49: They are not absolutely accident free:
http://crazifornia.com/category/the-blog/
Buried steel pipe does eventually corrode
And underground, breaks and leaks may go undetected => Explosions / Fires
Producing, in recent years, these well known gas leaks & explosions:
2010 - San Bruno California 1994 - Edison New Jersey:
8 dead 1 dead (1500 evacuated, 100 homeless)
http://spectrabusters.org/2014/02/21/spectras-durham-woods-apartment-fire-edison-nj-1994/

## Slide 50: I looked for safety cross-comparisons of these transportation modes
1) http://www.rita.dot.gov/bts/sites/rita.dot.gov.bts/files/publications/national_transportation_statistics/index.html
2) http://www.rita.dot.gov/bts/sites/rita.dot.gov.bts/files/publications/national_transportation_statistics/html/table_02_06.html
3) http://www.rita.dot.gov/bts/sites/rita.dot.gov.bts/files/publications/national_transportation_statistics/index.html#chapter_2
U.S. Department of Transportation1 had highway and rail data (only):
"Hazardous Materials Fatalities, Injuries, Accidents & Property Damage" 2
Their Table 2.6 was way to big3 to insert here, so I've excerpted just parts of it:
2000 2002 2004 2006 2008 2010 2012
Hazmat highway fatalities: 16 8 10 6 6 8 12
Hazmat rail fatalities: 0 1 3 0 0 0 0
Hazmat highway injuries: 164 118 155 192 150 152 144
Hazmat rail injuries: 82 14 122 25 63 38 18
Hazmat highway incidents: 15.0k 15.5k 13k 17.2k 14.8k 12.7k 13.2k
Hazmat rail incidents: 1.1k 0.9k 0..8k 0.7k 0.7k 0.7k 0.7k
Table supports my expectation that rail safety is superior to highway safety
It is also my impression is that pipeline safety is superior to both of those

## Slide 51: Bringing us to a final topic: Energy Investment
You most frequently hear about this in discussions (arguments) about solar cells
For PV, a key metric is called the cell's Energy Payback Time (EPBT)
= Time a solar cell would have to be operated
to generate energy equal to the total energy invested in it
This is NOT just the energy used to operate that solar cell or solar farm!
Instead, for every raw material and component used in that solar cell / solar farm
You must add in ALL of the energy used for:
Mining + refining + transportation + manufacture + operation +
decomissioning + disposal + recycling + reclamation
Making this a LIFE CYCLE ASSESSMENT (or LCA)

## Slide 52: Data on Energy Payback Time (EPBT) for Solar Cells:
Source: p. 84, Solar Generation 6 – European Photovoltaic Energy Association
http://www.greenpeace.org/international/Global/international/publications/climate/2011/Final%20SolarGeneration%20VI%20full%20report%20lr.pdf
From the European Photovoltaic Energy Association:
Contributing factors & steps:
Si PV does have longer EPBT:
1.75 years for mono Si PV
vs.
0.8 years for CdTe PV
Conventional Silicon
Non-Silicon & ultrathin Si

## Slide 53: From a less partisan source:
How Long Does it Take for Photovoltaics To Produce the Energy Used
PE Magazine, Society of Professional Engineers, February 2012
http://www.clca.columbia.edu/236_PE_Magazine_Fthenakis_2_10_12.pdf
U.S. National Society of Professional Engineers:
This neutral source agrees well with preceding trade association data!

## Slide 54: But when you think about it, EPBT is a rather dumb metric:
Because, while two types of cell might have the same EPBT (= energy in),
One might produce energy for 2X as long (e.g., by using Xtal vs. poly Si)
Instead, what we clearly need (for EVERY energy technology!) is the RATIO of:
Lifetime Energy Produced / Lifetime Energy Invested
Where BOTH numerator and denominator must include ALL energies
For every single material & component used for/in that technology
from the absolute beginning of the process to the absolute end
This much more broadly applied figure of merit is called :
Energy Return on Investment (EROI)
Or, less ambiguously: Energy Return on Invested Energy (EROIE)

## Slide 55: Energy Return on Investment (EROI) for energy technologies:
1) D.J. Murphy & C.A.S. Hall, "Year in review EROI or energy return on (energy) invested". Annals of the New York Academy of Sciences 1185, pp. 102–118 (2010)
Here from the seminal (i.e., pioneering) publication on EROI's :1
Which, rather surprisingly, did not come out until 2010!

## Slide 56: Newer EROI data (from multiple original sources): 1
1) The True Cost of Fossil Fuels, Mason Inman, Scientific American, April 2013
Technology EROI
Liquid Fuels:
Conventional oil 16
Ethanol from sugarcane 9
Biodiesel from soy 5.5
Tar Sands 5
  Heavy oil from California 4
Ethanol from corn 1.4
Electricity from:
Hydroelectric Dams 40+
Wind 20
Coal 18
Natural Gas 7
Solar PV 6
Nuclear 5
Color coded to reflect claim that economic viability requires EROI of at least 5

## Slide 57: But it's very difficult to evaluate full lifetime energies
Energy payback time (EPBT) and energy return on investment (EROI) of solar photovoltaic systems: A systematic review and meta-analysis, Khagendra P. Bhandari et al., Renewable and Sustainable Energy Reviews 47, pp. 133-141 (2015)
So many researchers have worked to further refine such calculations
Particular attention has been paid to calculation of photovoltaic number(s)
Including efficiency change over lifetime of different PV technologies
And differences between the lifetimes themselves
2015 "meta-data" analysis of 232 peer-reviewed studies computed EROI's of:
Mono-crystalline Si PV = 8.7
Poly-crystalline Si PV = 11.6
Amorphous Si PV = 14.5
CdTe PV = 34.2
CIGS PV = 19.9

## Slide 58: Adding in more extensive Si PV data (single crystal vs. poly vs. amorphous):
Technology EROI
Liquid Fuels:
Conventional oil 16
Ethanol from sugarcane 9
Biodiesel from soy 5.5
Tar Sands 5
Heavy oil from California 4
Ethanol from corn 1.4
Electricity from:
Hydroelectric Dams 40+
Wind 20
Coal 18
Natural Gas 7
Solar PV using Si 6-15
Nuclear 5
Color coded to reflect claim that economic viability requires EROI of at least 5

## Slide 59: Take a moment to truly absorb these very important results:
1) The True Cost of Fossil Fuels, Mason Inman, Scientific American, April 2013
Noting Scientific American's claim that economically viable EROI must be at least 5 1
Champions, in descending order:
Hydro (40+), CdTe PV (34.2), Wind (20), CIGS PV (19.9), Coal (18), Oil (16)
Weaker but still viable:
poly-Si PV (11.6), Sugarcane Ethanol (9), mono-Si PV (8.7), Natural Gas (7)
Marginal:
Soy Biodiesel (5.5), Tar Sands (5), Nuclear (5)
Apparently non-viable:
Heavy Calif Oil (4), Corn Ethanol (1.4)
But looking more closely at those orange highlighted fossil fuel cases:

## Slide 60: EROIs evolve with new raw material reserves & extraction technologies:
1) The True Cost of Fossil Fuels, Mason Inman, Scientific American, April 2013
2) EROI of Different Fuels and Implications for Society, C.A.S. Hall et al., Energy Policy 64, pp. 141-52 (2014)
With harder-to-extract new reserves, classic fossil fuel EROI's are falling: 1, 2
Steam injection (to liquefy "heavy" viscous oil) causes EROI to plummet
From previous page: EROI drops from 16 to a ~ non-viable value of 4
New non-strip mining extraction of tar sands adds same steam injection technique
It's thus likely that steam-extracted tar sand EROI will be ~ 1 (i.e., 5/4)
(and I've seen data supporting this contention)

## Slide 61: Conclusions: Notice a recurring pattern?
I opened this note set with some "common wisdoms" about energy technologies
But when I more carefully explored many such contentions, I found:
A germ of reality, but one which was undercut (or even overturned!)
by fuller facts and numbers
The "Gray Void" is FILLED
with such disconnects between sound bites and reality
FACTS are almost always more subtle, nuanced, and less straightforward

## Slide 62: Credits / Acknowledgements
Some materials used in this class were developed under a National Science Foundation "Research Initiation Grant in Engineering Education" (RIGEE).
Other materials, including the "Virtual Lab" science education website, were developed under even earlier NSF "Course, Curriculum and Laboratory Improvement" (CCLI) and "Nanoscience Undergraduate Education" (NUE) awards.
This set of notes was authored by John C. Bean who also created all figures not explicitly credited above.
Copyright John C. Bean
(However, permission is granted for use by individual instructors and students in non-profit academic institutions)
An Introduction to Sustainable Energy Systems: WeCanFigureThisOut.org/ENERGY/Energy_home.htm